## Slide 1
The steps for assembling TRA CHANG power tiller

## Slide 2
How to assemble
Assemble the hitch
(Hitch must on the left side of power tiller)
1
Assemble the frame front
2
Assemble the cage wheels
3
Assemble the wheel to the wheel axle.
4
Correct wheel assembly, The wheel blades must point to back of power tiller.

## Slide 3
The steps for assembling KUBOTA diesel engine with TRA CHANG power tiller

## Slide 4
Pull the engine to the front.
Keep the belt tight and tighten the nut.
Remove the engine from the stand.
1
Assemble the engine to the chassis of the power tiller and tighten the engine nut
2
4
5
3
Attach the pulley to the flywheel.
Attach the belt to the pulley on the power tiller and the engine.
Adjust the tension of the belt
about 22-28 mm by tightening
or loosen the nut.
6
Loosen 2 nuts at accelerator allowing the accelerator lever to work independently. Then tighten again.
7
Attach the accelerator cable to the accelerator lever and tighten the nut
8
How to assemble